## Slide 1: AER 1216 – Fundamentals of UAVs
Lecture 12 - Quadrotor Dynamics and Control II
Karime Pereida, Ph.D.
Prof. Angela Schoellig

## Slide 2: Quadrotor Dynamics and Control I
Motivation
  Quadrotors require controllers to work well
How does a quadrotor move?
  Varying motor speeds
What is the quadrotor control architecture?
  Nested control architecture
How to control a 1D quadrotor?
  PD controller for a 1D quadrotor
Simulator and initial control exploration

## Slide 3: Quadrotor Dynamics and Control Lectures
Lecture 1 | Lecture 2 | Lecture 3
Introduction to quadrotor control Controlling the up-down motion of the quadrotor | Controlling the quadrotor in 2D (y-z plane) Introduction to nonlinear controllers | Controlling the quadrotor in 3D Setting up a commercially available quadrotor
Installing simulator and initial controller exploration | Applying a 2D controller to the simulated quadrotor | How to set up a commercially available quadrotor
Inspired by Vijay Kumar’s Aerial Robotics Coursera course https://www.coursera.org/learn/robotics-flight

## Slide 4: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
  Planar (2D) quadrotor model
  Linearization
  Nested control loop
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 5: Planar (2D) Quadrotor Model
Newton’s equations of motion:
Euler’s equations of motion:
Thrust
Moment

## Slide 6: Planar (2D) Quadrotor Model
State space:
Thrust
Moment

## Slide 7: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
  Planar (2D) quadrotor model
  Linearization
  Nested control loop
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 8: Linearization
Helps us to control nonlinear systems around equilibrium points.
Insight of stability around equilibrium points (Lyapunov linearization method).
For nonlinear systems of the following form: with equilibrium point .
Use Taylor first-order expansion:
E.g.,
Equilibrium point:
Linearization through Taylor expansion:

## Slide 9: Linearized Dynamics Model
Nonlinear equations of motion:
Linearize around the equilibrium hover configuration:
Linearized dynamics around hover (first-order Taylor expansion):

## Slide 10: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
  Planar (2D) quadrotor model
  Linearization
  Nested control loop
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 11: 2D Trajectory Tracking Problem Statement
Given the 2D planar quadrotor, design a controller to follow the desired differentiable trajectory
Desired trajectory
(pos., vel., accel.)
2. Define control objective:
Make decay exponentially to 0
1. Define error:
3. Choose appropriate controller.

## Slide 12: Nested Control Architecture
Cost
Function
High-Level Task
Features
Assume that yaw is controlled to a constant value
Angles + angular rates
Attitude Ctrl
Angle and angular rates
Meas./Estimates
High-level Objective
We focus on calculating thrust and moment (motor control is typically proportional)
Position Ctrl
Position + Yaw
Position
+ Yaw
Moment
Motion
Motor Ctrl
Measured Turn Rates
Thrust

## Slide 13: Nested Control Architecture
Attitude Ctrl
Angle and angular rates
Meas./Estimates
Angles + angular rates
Moment
Motion

## Slide 14: Attitude Controller
Attitude
Controller
Make decay exponentially to 0:
Linearized dynamics:
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 15: Nested Control Architecture
Attitude Ctrl
Angle and angular rates
Meas./Estimates
Angles + angular rates
Moment
Motion
Position Ctrl
Position + Yaw
Position
+ Yaw

## Slide 16: Position Controller
Attitude
Controller
Make decay exponentially to 0:
Linearized dynamics:
Position
Controller
Shape as a first-order system:
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 17: Nested Control Architecture
Attitude Ctrl
Angle and angular rates
Meas./Estimates
Angles + angular rates
Moment
Motion
Position Ctrl
Position + Yaw
Position
+ Yaw
Thrust

## Slide 18: Position Controller
Attitude
Controller
Make decay exponentially to 0:
Linearized dynamics:
Position
Controller
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 19: Nested Control Architecture
Cost
Function
High-Level Task
Features
Angles + angular rates
Attitude Ctrl
Angle and angular rates
Meas./Estimates
High-level Objective
Position Ctrl
Position + Yaw
Position
+ Yaw
Moment
Motion
Motor Ctrl
Measured Turn Rates
Thrust

## Slide 20: Control Equations
Simplification with no performance reduction
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 21: Control Equations
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 22: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
What other linear controllers can we use?
  Pole placement
  Linear Quadratic Regulator (LQR)
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 23: Linear Controllers
Pole placement:
Consider the linearized dynamics of our system:
The closed-loop system for input is given by:
If the pair is controllable (input can move the state from any initial state to any final state in finite time), then there exists a feedback matrix such that the closed-loop eigenvalues can be placed in arbitrary locations.
We can choose the behavior of the closed-loop system
Where to place the eigenvalues?
Notes: A = np.array([[0, 0, 0, 1, 0, 0], [0, 0, 0, 0, 1, 0], [0, 0, 0, 0, 0, 1], [0, 0, -self.g, 0, 0, 0], [0, 0, 0, 0, 0, 0], [0, 0, 0, 0, 0, 0]]) B = np.array([[0, 0], [0, 0], [0, 0], [0, 0], [1/self.mass, 0], [0, 1/self.inertia_xx]]) cont = np.concatenate((B, A.dot(B), A.dot(A.dot(B)), A.dot(A.dot(A.dot(B))), A.dot(A.dot(A.dot(A.dot(B)))), A.dot(A.dot(A.dot(A.dot(A.dot(B))))) ), axis=1)

## Slide 24: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
What other linear controllers can we use?
  Pole placement
  Linear Quadratic Regulator (LQR)
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 25: Linear Controllers
Linear Quadratic Regulator (LQR):
Operate the dynamic system at a minimum cost. (Optimal control)
Cost is described by a quadratic function.
System described by set of linear differential equations.
For discrete-time systems:
Optimal control sequence minimizing cost is:
penalize error
penalize control effort
static gain
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 26
Q&A
Break

## Slide 27: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 28: When should we use nonlinear controllers?
Which type of controller (linear/nonlinear) does each drone have?

## Slide 29: When should we use nonlinear controllers?
The task was to fly at 1 m. However, one drone is not able to achieve this.
What type of controller does it have?

## Slide 30: When should we use nonlinear controllers?
Why is this happening?
Linearization is neglecting the effect of the roll angle in the system thrust.
Nonlinear dynamics:
Linearized dynamics:
In other words: modeling errors
Notes: Focus on the attitude controller. U2 s.t. phi (differentiable) goes to the desired value.
Look at equations of motion. Relate u2 and phi.
Relate phi and ydd.

## Slide 31: When should we use nonlinear controllers?
Triple flip with a quadrotor
Time-optimized slalom
Fast path following with a ground vehicle
..
S. Schaal and C. G. Atkeson, “Learning control in robotics,”
IEEE Robotics & Automation Magazine, vol. 17, no. 2, pp. 20–29, 2010.
When we want to perform aggressive Maneuvers
Notes: That is, there is a computer that controls one or multiple robots at the same time. Specifically, I have been working with unmanned aerial vehicles for the past 6 years – these are so-called quadrocopters. They have four rotors that can be controlled separately and enable very agile, aggressive maneuvers.

## Slide 32: Triple Adaptive Flips
youtu.be/bWExDW9J9sA

## Slide 33: Slalom Learning
youtu.be/zHTCsSkmADo

## Slide 34: Visual Teach and Repeat
youtu.be/08_d1HSPADA

## Slide 35: When should we use nonlinear controllers?
Unmodelled dynamics
Unknown external disturbances
  (e.g., environment conditions such as wind, unknown payload, topography or weather)
  Model inaccuracies limit achievable performance!
Notes: That is, there is a computer that controls one or multiple robots at the same time. Specifically, I have been working with unmanned aerial vehicles for the past 6 years – these are so-called quadrocopters. They have four rotors that can be controlled separately and enable very agile, aggressive maneuvers.

## Slide 36: Nonlinear Controllers
Disturbances include modeling errors
Robust Control: controller is guaranteed to be stable for all possible realizations of the disturbance
  Handles rapidly changing disturbances
  Tends to be conservative
Adaptive Control: controller adapts based on parameters estimated using state measurements during execution
  Slow-varying disturbances
  Could present unwanted effects such as chattering
Notes: A = np.array([[0, 0, 0, 1, 0, 0], [0, 0, 0, 0, 1, 0], [0, 0, 0, 0, 0, 1], [0, 0, -self.g, 0, 0, 0], [0, 0, 0, 0, 0, 0], [0, 0, 0, 0, 0, 0]]) B = np.array([[0, 0], [0, 0], [0, 0], [0, 0], [1/self.mass, 0], [0, 1/self.inertia_xx]]) cont = np.concatenate((B, A.dot(B), A.dot(A.dot(B)), A.dot(A.dot(A.dot(B))), A.dot(A.dot(A.dot(A.dot(B)))), A.dot(A.dot(A.dot(A.dot(A.dot(B))))) ), axis=1)

## Slide 37: Nonlinear Controllers
Disturbances include modeling errors
Learning-based Control: controller improves performance by learning features (e.g. model) of the system
  Performance can improve over time
  Lack of stability guarantees
Optimal Control: controller optimizes the performance based on a predefined cost function
  Performance depends on model quality
  Could be computationally expensive
Controllers can be combined to improve their characteristics!
Notes: A = np.array([[0, 0, 0, 1, 0, 0], [0, 0, 0, 0, 1, 0], [0, 0, 0, 0, 0, 1], [0, 0, -self.g, 0, 0, 0], [0, 0, 0, 0, 0, 0], [0, 0, 0, 0, 0, 0]]) B = np.array([[0, 0], [0, 0], [0, 0], [0, 0], [1/self.mass, 0], [0, 1/self.inertia_xx]]) cont = np.concatenate((B, A.dot(B), A.dot(A.dot(B)), A.dot(A.dot(A.dot(B))), A.dot(A.dot(A.dot(A.dot(B)))), A.dot(A.dot(A.dot(A.dot(A.dot(B))))) ), axis=1)

## Slide 38: Learning and Adaptive Controllers
Learning and adaptation enable
safe, high-performance motions
in uncontrolled, unknown or changing environments

## Slide 39: Research Focus
Prior information
Which motions are feasible?
How to plan collision-free motions?
+ Current sensor measurement
How to guide the vehicle along a desired path?
+ Past experiment data
Can the performance be improved by leveraging past data?
Towards robotics applications
DYNAMICS
ROBOTICS
MACHINE LEARNING
CONTROLS

## Slide 40: Learning-based Robust Control
youtu.be/YqhLnCm0KXY

## Slide 41: Development Process
Specific task, adaptation of a few input parameters only
General task, full input trajectory adaptation
Learning with safety guarantees
Model learning, anytime learning
True model
Nominal model

## Slide 42: Importance of Nonlinear Controllers
DYNAMICS
ROBOTICS
MACHINE LEARNING
CONTROLS
Safe, reliable, high-performance flight of single or multiple aerial vehicles in changing and unknown conditions using a combination of a-priori models and data
Notes: That is, there is a computer that controls one or multiple robots at the same time. Specifically, I have been working with unmanned aerial vehicles for the past 6 years – these are so-called quadrocopters. They have four rotors that can be controlled separately and enable very agile, aggressive maneuvers.

## Slide 43: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 44: Nonlinear Controller 1
Nonlinear equations of motion:
We calculate such that the errors decay exponentially to 0.
Using , the nonlinear equations of motion, and measured , we solve for :
Using , the nonlinear equations of motion, and , we solve for :
Shape as a first-order system:

## Slide 45: Nonlinear Controller 2
Nonlinear equations of motion:
We calculate such that the errors decay exponentially to 0.
We have a system of two equations and two unknowns . Solve for :
Shape as a first-order system:

## Slide 46: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
  Linearize dynamics and apply PD controller
What other linear controllers can we use?
  Pole placement and LQR
When should we use nonlinear controllers?
  When system behavior deviates from linearization
How to nonlinearly control a planar (2D) quadrotor?
  Nested architecture, nonlinear eq’s and measurements
How to control the planar quadrotor in simulation?

## Slide 47
Q&A
Break

## Slide 48: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
What other linear controllers can we use?
When should we use nonlinear controllers?
How to nonlinearly control a planar (2D) quadrotor?
How to control the planar quadrotor in simulation?

## Slide 49: Quadrotor Frames
Quadrotor reference frames:
Please download the code at:
https://github.com/JacopoPan/gym-pybullet-drones/releases/tag/v0.5.2

## Slide 50: Linear Controller
Controller equations:
How to compute motor turn rates?
Hint 1: Think about sum of forces and torques
Hint 2: The quadrotor must move in the plane only without yaw movement.
Hint 3: How do the forces and moments relate to motor turn rates?

## Slide 51: Linear vs Nonlinear Controller
Nonlinear controller 1 Nonlinear controller 2 Linear controller

## Slide 52: Useful Variables and Functions
Variables:
Gravity: self.g
Quadrotor mass: self.mass
Quadrotor moment of inertia around x axis: self.inertia_xx
: y_ddot
: z_ddot
: roll_ddot
: current_rpy[0]
Basic math and NumPy:
: np.sin(x)
: np.cos(x)
: x**2
: np.sqrt(x)
Modify the code at the four appropriate places denoted by
“Objective n of 4”.

## Slide 53: Quadrotor Dynamics and Control II
How to linearly control a planar (2D) quadrotor?
  Linearize dynamics and apply PD controller
What other linear controllers can we use?
  Pole placement and LQR
When should we use nonlinear controllers?
  When system behavior deviates from linearization
How to nonlinearly control a planar (2D) quadrotor?
  Nested architecture, nonlinear eq’s and measurements
How to control the planar quadrotor in simulation?